Presentation to Utility MACT Stakeholder Group

December 18, 2001

By Ranking Workgroup:

Felice Stadler

Pat Raher

Praveen Amar

Using the spreadsheet provided by the U.S. EPA, we were asked to rank the stack test data, and anticipate some of the questions that may be raised during this process.

The workgroup agreed that the first step was to rank the coal-fired boilers using, what we referred to as, “value neutral” criteria.  In other words, we did not rank by boiler type, fuel type, or stack controls.

Our goal was to rank boilers based on their performance, which we defined in terms of the rate of mercury emitted from the stack.  We intended to rank the boilers in two ways: 1. lbs/TBtu (F factor); 2. lbs/MWh.  With the data supplied by EPA we were able to do the first part; additional data will need to be compiled (specifically the heat rate of each boiler) in order to calculate an output-based emission rate.

Ranking the data by just looking at what comes out of the stack allowed us to gain a better understanding of the operations of the top performing fleet (boiler type, fuel type, existing controls).

Below is a profile of the top ten plants (those with the lowest lbs/TBtu emission rate.  (Refer to Maxwell’s definitions for explanation of abbreviations.)

Top 10 (lbs/TBtu from 0.0816-0.3348):

Boiler type:

3 FBC

1 Stoker

6 PC

Fuel type (during test):

2 waste bit.

1 bit./pet coke

7 bit.

PM controls:

9 baghouses

1 ESP-CS

NOx controls:

4 NOx combustion (see Maxwell’s definitions)

2 SNCR

2 SCR

2 no controls

SO2 controls:

3 FBC

4 SDA

2 compliant coal

1 wet scrubber

Attached are several tables ranking the stack test data by emission rate (lb/TBtu), and then emission rate grouped by boiler type and fuel type.  This was done to help illustrate that variation exists—in some cases it is significant.

The bottom line is that the performance of an individual boiler depends on a combination of factors, including things like boiler efficiency, which need to be considered collectively.

A necessary next step is calculating an output-based emission rate to ensure that this option is on the table.  This is the only method that guarantees the inclusion of boiler efficiency as one of the methods for achieving higher performance (i.e., a lower emission rate).

Ranked by lb/TBtu

| Plant name | Unit name | Boiler Type | PM control | FGD | Fuel in test | F factor lb/TBtu out control |
| --- | --- | --- | --- | --- | --- | --- |
| Kline Township Cogen Facility | GEN1 | FBC | BAGHOUSE |  | WASTE B | 0.0816 |
| Scrubgrass Generating Company L.P. | GEN1 | FBC | BAGHOUSE |  | WASTE B | 0.0936 |
| Mecklenburg Cogeneration Facility | GEN 1 | PC | BAGHOUSE |  | B | 0.1062 |
| Dwayne Collier Battle Cogeneration Facility | 2B | STOKER | BAGHOUSE |  | B | 0.1074 |
| Valmont | 5 | PC | BAGHOUSE |  | B | 0.1268 |
| Stockton Cogen Company | GEN1 | FBC | BAGHOUSE |  | B/PET | 0.1316 |
| SEI - Birchwood Power Facility | 1 | PC | BAGHOUSE |  | B | 0.2379 |
| Intermountain | 2SGA | PC | BAGHOUSE | Y | B | 0.2466 |
| Logan Generating Plant | GEN 1 | PC | BAGHOUSE |  | B | 0.2801 |
| Salem Harbor | 3 | PC | ESP-CS |  | B | 0.3348 |
| Clover Power Station | 2 | PC | BAGHOUSE | Y | B | 0.3529 |
| AES Hawaii, Inc. | A | FBC | BAGHOUSE |  | SB | 0.4606 |
| Clay Boswell | 2 | PC | BAGHOUSE |  | SB | 0.6633 |
| Craig | C3 | PC | BAGHOUSE |  | SB | 0.7248 |
| W.H. Sammis | 1 | PC | BAGHOUSE |  | B | 0.8291 |
| Charles R. Lowman | 2 | PC | ESP-HS | Y | B | 0.9706 |
| Shawnee Fossil Plant | 3 | PC | BAGHOUSE |  | B/SB | 1.0507 |
| Cholla | 3 | PC | ESP-HS |  | SB | 1.2066 |
| Presque Isle | 6 | PC | ESP-CS |  | B/PET | 1.2217 |
| Presque Isle | 5 | PC | ESP-CS |  | B/PET | 1.2622 |
| Widows Creek Fossil Plant | 6 | PC | ESP-CS |  | B | 1.3986 |
| Craig | C1 | PC | ESP-HS | Y | SB | 1.4456 |
| Big Bend | BB03 | TURBO | ESP-CS | Y | B | 1.5652 |
| Valley | 2 | PC | BAGHOUSE |  | B/PET | 1.6630 |
| Meramec | 4 | PC | ESP-CS |  | SB/B | 1.7255 |
| AES Cayuga (NY) (formerly NYSEG Milliken) | 2 | PC | ESP-CS | Y | B | 2.0652 |
| R.D. Morrow, Sr. Generating Plant | 2 | PC | ESP-HS | Y | B | 2.1269 |
| Nelson Dewey | 1 | CYCLONE | ESP-HS |  | SB/PET | 2.1349 |
| Bailly | 7 | CYCLONE | ESP-CS | Y | B | 2.2306 |
| Coronado | U1B | PC | ESP-HS | Y | SB | 2.4468 |
| Comanche | 2 | PC | BAGHOUSE |  | SB | 2.5931 |
| Navajo | 3 | PC | ESP-HS | Y | B | 2.7359 |
| Jack Watson | 4 | PC | ESP-CS |  | B | 2.9333 |
| Laramie River Station | 1 | PC | ESP-CS | Y | SB | 3.0184 |
| Cholla | 2 | PC | MECH/PARTSCRUB | Y | SB | 3.1864 |
| Brayton Point | 1 | PC | ESP-CS |  | B | 3.2000 |
| Laramie River Station | 3 | PC | ESP-CS |  | SB | 3.3411 |
| Bay Front Plant | 5 | CYCLONE | MECH |  | B | 3.5792 |
| Brayton Point | 3 | PC | ESP-CS |  | B | 3.6979 |
| St. Clair Power Plant | 4 | PC | ESP-CS |  | SB/B | 3.9076 |
| R.M. Heskett Station | B2 | FBC | ESP-CS |  | L | 3.9768 |
| Antelope Valley Station | B1 | PC | BAGHOUSE |  | L | 4.0042 |
| Leland Olds Station | 2 | CYCLONE | ESP-CS |  | L | 4.0233 |
| Clay Boswell | 3 | PC | PARTSCRUB | Y | SB | 4.0454 |
| San Juan | 2 | PC | ESP-HS | Y | SB | 4.2854 |
| Cliffside | 1 | PC | ESP-HS |  | B | 4.3223 |
| Clay Boswell | 4 | PC | PARTSCRUB | Y | SB | 4.4550 |
| Jim Bridger | BW 74 | PC | ESP-CS | Y | SB | 4.7040 |
| Presque Isle | 9 | PC | ESP-HS |  | SB | 5.0738 |
| Lawrence | 4 | PC | PARTSCRUB | Y | SB | 5.1181 |
| Wabash River Generating Station | 1 + 1A | COAL GAS | NONE |  | B | 5.3343 |
| Polk Power | 1 | COAL GAS | NONE |  | B | 5.4713 |
| La Cygne | 1 | CYCLONE | PARTSCRUB | Y | SB | 5.5140 |
| Colstrip | 3 | PC | PARTSCRUB | Y | SB | 5.7264 |
| Montrose | 1 | PC | ESP-CS |  | SB | 5.8573 |
| Gaston | 1 | PC | ESP-HS |  | B | 6.0738 |
| Stanton Station | 10 | PC | BAGHOUSE |  | L | 6.2517 |
| Port Washington | 4 | PC | ESP-CS |  | B | 6.6916 |
| Dunkirk | 2 | PC | ESP-HS |  | B | 6.8030 |
| Clifty Creek | 6 | PC | ESP-HS |  | SB/B | 6.8745 |
| Stanton Station | 1 | PC | ESP-CS |  | L | 6.9024 |
| Newton | 2 | PC | ESP-CS |  | SB | 6.9877 |
| Wyodak | BW 91 | PC | ESP-CS |  | SB | 7.0701 |
| Bruce Mansfield | 1 | PC | PARTSCRUB |  | B | 7.0985 |
| Sherburne County Generating Plant | #3 | PC | BAGHOUSE |  | SB | 7.5401 |
| George Neal South | 4 | PC | ESP-CS |  | SB | 7.7269 |
| Rawhide | 101 | PC | BAGHOUSE |  | SB | 7.7630 |
| Coyote | 1 | CYCLONE | BAGHOUSE |  | L | 7.9523 |
| Sam Seymour | 3 | PC | ESP-CS | Y | SB | 8.6353 |
| GRDA | 2 | PC | ESP-CS |  | SB/B | 8.6918 |
| Gibson Generating Station (1099) | 3 | PC | ESP-CS |  | B | 9.7452 |
| Columbia | 1 | PC | ESP-HS |  | SB | 10.3097 |
| Platte | 1 | PC | ESP-HS |  | SB | 10.6121 |
| Lewis & Clark | B1 | PC | PARTSCRUB |  | L | 10.8315 |
| TNP-One | U2 | FBC | BAGHOUSE |  | L | 10.8596 |
| Limestone | LIM1 | PC | ESP-CS | Y | L | 13.6612 |
| Monticello | 3 | PC | ESP-CS | Y | L | 18.3232 |
| Gibson Generating Station (0300) | 3 | PC | ESP-CS |  | B | 29.0614 |
| Big Brown | 1 | PC | ESP-CS/BAGHOUSE |  | L | 30.0889 |
| Monticello | 1 | PC | ESP-CS/BAGHOUSE |  | L | 55.8686 |

Ranked by lb/TBtu and boiler type

| Plant name | Unit name | Boiler Type | PM control | FGD | Fuel in test | F factor lb/TBtu out control |
| --- | --- | --- | --- | --- | --- | --- |
| Nelson Dewey | 1 | CYCLONE | ESP-HS |  | SB/PET | 2.1349 |
| Bailly | 7 | CYCLONE | ESP-CS | Y | B | 2.2306 |
| Bay Front Plant | 5 | CYCLONE | MECH |  | B | 3.5792 |
| Leland Olds Station | 2 | CYCLONE | ESP-CS |  | L | 4.0233 |
| La Cygne | 1 | CYCLONE | PARTSCRUB | Y | SB | 5.5140 |
| Coyote | 1 | CYCLONE | BAGHOUSE |  | L | 7.9523 |
| Kline Township Cogen Facility | GEN1 | FBC | BAGHOUSE |  | WASTE B | 0.0816 |
| Scrubgrass Generating Company L.P. | GEN1 | FBC | BAGHOUSE |  | WASTE B | 0.0936 |
| Stockton Cogen Company | GEN1 | FBC | BAGHOUSE |  | B/PET | 0.1316 |
| AES Hawaii, Inc. | A | FBC | BAGHOUSE |  | SB | 0.4606 |
| R.M. Heskett Station | B2 | FBC | ESP-CS |  | L | 3.9768 |
| TNP-One | U2 | FBC | BAGHOUSE |  | L | 10.8596 |
| Mecklenburg Cogeneration Facility | GEN 1 | PC | BAGHOUSE |  | B | 0.1062 |
| Valmont | 5 | PC | BAGHOUSE |  | B | 0.1268 |
| SEI - Birchwood Power Facility | 1 | PC | BAGHOUSE |  | B | 0.2379 |
| Intermountain | 2SGA | PC | BAGHOUSE | Y | B | 0.2466 |
| Logan Generating Plant | GEN 1 | PC | BAGHOUSE |  | B | 0.2801 |
| Salem Harbor | 3 | PC | ESP-CS |  | B | 0.3348 |
| Clover Power Station | 2 | PC | BAGHOUSE | Y | B | 0.3529 |
| Clay Boswell | 2 | PC | BAGHOUSE |  | SB | 0.6633 |
| Craig | C3 | PC | BAGHOUSE |  | SB | 0.7248 |
| W.H. Sammis | 1 | PC | BAGHOUSE |  | B | 0.8291 |
| Charles R. Lowman | 2 | PC | ESP-HS | Y | B | 0.9706 |
| Shawnee Fossil Plant | 3 | PC | BAGHOUSE |  | B/SB | 1.0507 |
| Cholla | 3 | PC | ESP-HS |  | SB | 1.2066 |
| Presque Isle | 6 | PC | ESP-CS |  | B/PET | 1.2217 |
| Presque Isle | 5 | PC | ESP-CS |  | B/PET | 1.2622 |
| Widows Creek Fossil Plant | 6 | PC | ESP-CS |  | B | 1.3986 |
| Craig | C1 | PC | ESP-HS | Y | SB | 1.4456 |
| Valley | 2 | PC | BAGHOUSE |  | B/PET | 1.6630 |
| Meramec | 4 | PC | ESP-CS |  | SB/B | 1.7255 |
| AES Cayuga (NY) (formerly NYSEG Milliken) | 2 | PC | ESP-CS | Y | B | 2.0652 |
| R.D. Morrow, Sr. Generating Plant | 2 | PC | ESP-HS | Y | B | 2.1269 |
| Coronado | U1B | PC | ESP-HS | Y | SB | 2.4468 |
| Comanche | 2 | PC | BAGHOUSE |  | SB | 2.5931 |
| Navajo | 3 | PC | ESP-HS | Y | B | 2.7359 |
| Jack Watson | 4 | PC | ESP-CS |  | B | 2.9333 |
| Laramie River Station | 1 | PC | ESP-CS | Y | SB | 3.0184 |
| Cholla | 2 | PC | MECH/PARTSCRUB | Y | SB | 3.1864 |
| Brayton Point | 1 | PC | ESP-CS |  | B | 3.2000 |
| Laramie River Station | 3 | PC | ESP-CS |  | SB | 3.3411 |
| Brayton Point | 3 | PC | ESP-CS |  | B | 3.6979 |
| St. Clair Power Plant | 4 | PC | ESP-CS |  | SB/B | 3.9076 |
| Antelope Valley Station | B1 | PC | BAGHOUSE |  | L | 4.0042 |
| Clay Boswell | 3 | PC | PARTSCRUB | Y | SB | 4.0454 |
| San Juan | 2 | PC | ESP-HS | Y | SB | 4.2854 |
| Cliffside | 1 | PC | ESP-HS |  | B | 4.3223 |
| Clay Boswell | 4 | PC | PARTSCRUB | Y | SB | 4.4550 |
| Jim Bridger | BW 74 | PC | ESP-CS | Y | SB | 4.7040 |
| Presque Isle | 9 | PC | ESP-HS |  | SB | 5.0738 |
| Lawrence | 4 | PC | PARTSCRUB | Y | SB | 5.1181 |
| Colstrip | 3 | PC | PARTSCRUB | Y | SB | 5.7264 |
| Montrose | 1 | PC | ESP-CS |  | SB | 5.8573 |
| Gaston | 1 | PC | ESP-HS |  | B | 6.0738 |
| Stanton Station | 10 | PC | BAGHOUSE |  | L | 6.2517 |
| Port Washington | 4 | PC | ESP-CS |  | B | 6.6916 |
| Dunkirk | 2 | PC | ESP-HS |  | B | 6.8030 |
| Clifty Creek | 6 | PC | ESP-HS |  | SB/B | 6.8745 |
| Stanton Station | 1 | PC | ESP-CS |  | L | 6.9024 |
| Newton | 2 | PC | ESP-CS |  | SB | 6.9877 |
| Wyodak | BW 91 | PC | ESP-CS |  | SB | 7.0701 |
| Bruce Mansfield | 1 | PC | PARTSCRUB |  | B | 7.0985 |
| Sherburne County Generating Plant | #3 | PC | BAGHOUSE |  | SB | 7.5401 |
| George Neal South | 4 | PC | ESP-CS |  | SB | 7.7269 |
| Rawhide | 101 | PC | BAGHOUSE |  | SB | 7.7630 |
| Sam Seymour | 3 | PC | ESP-CS | Y | SB | 8.6353 |
| GRDA | 2 | PC | ESP-CS |  | SB/B | 8.6918 |
| Gibson Generating Station (1099) | 3 | PC | ESP-CS |  | B | 9.7452 |
| Columbia | 1 | PC | ESP-HS |  | SB | 10.3097 |
| Platte | 1 | PC | ESP-HS |  | SB | 10.6121 |
| Lewis & Clark | B1 | PC | PARTSCRUB |  | L | 10.8315 |
| Limestone | LIM1 | PC | ESP-CS | Y | L | 13.6612 |
| Monticello | 3 | PC | ESP-CS | Y | L | 18.3232 |
| Gibson Generating Station (0300) | 3 | PC | ESP-CS |  | B | 29.0614 |
| Big Brown | 1 | PC | ESP-CS/BAGHOUSE |  | L | 30.0889 |
| Monticello | 1 | PC | ESP-CS/BAGHOUSE |  | L | 55.8686 |
| Dwayne Collier Battle Cogeneration Facility | 2B | STOKER | BAGHOUSE |  | B | 0.1074 |
| Big Bend | BB03 | TURBO | ESP-CS | Y | B | 1.5652 |
| Wabash River Generating Station | 1 + 1A | COAL GAS | NONE |  | B | 5.3343 |
| Polk Power | 1 | COAL GAS | NONE |  | B | 5.4713 |

Ranked by lb/TBtu and fuel type

| Plant name | Unit name | Fuel in test | Boiler Type | PM control | FGD | F factor lb/TBtu out control |
| --- | --- | --- | --- | --- | --- | --- |
| Mecklenburg Cogeneration Facility | GEN 1 | B | PC | BAGHOUSE |  | 0.1062 |
| Dwayne Collier Battle Cogeneration Facility | 2B | B | STOKER | BAGHOUSE |  | 0.1074 |
| Valmont | 5 | B | PC | BAGHOUSE |  | 0.1268 |
| Stockton Cogen Company | GEN1 | B/PET | FBC | BAGHOUSE |  | 0.1316 |
| SEI - Birchwood Power Facility | 1 | B | PC | BAGHOUSE |  | 0.2379 |
| Intermountain | 2SGA | B | PC | BAGHOUSE | Y | 0.2466 |
| Logan Generating Plant | GEN 1 | B | PC | BAGHOUSE |  | 0.2801 |
| Salem Harbor | 3 | B | PC | ESP-CS |  | 0.3348 |
| Clover Power Station | 2 | B | PC | BAGHOUSE | Y | 0.3529 |
| W.H. Sammis | 1 | B | PC | BAGHOUSE |  | 0.8291 |
| Charles R. Lowman | 2 | B | PC | ESP-HS | Y | 0.9706 |
| Shawnee Fossil Plant | 3 | B/SB | PC | BAGHOUSE |  | 1.0507 |
| Presque Isle | 6 | B/PET | PC | ESP-CS |  | 1.2217 |
| Presque Isle | 5 | B/PET | PC | ESP-CS |  | 1.2622 |
| Widows Creek Fossil Plant | 6 | B | PC | ESP-CS |  | 1.3986 |
| Big Bend | BB03 | B | TURBO | ESP-CS | Y | 1.5652 |
| Valley | 2 | B/PET | PC | BAGHOUSE |  | 1.6630 |
| AES Cayuga (NY) (formerly NYSEG Milliken) | 2 | B | PC | ESP-CS | Y | 2.0652 |
| R.D. Morrow, Sr. Generating Plant | 2 | B | PC | ESP-HS | Y | 2.1269 |
| Bailly | 7 | B | CYCLONE | ESP-CS | Y | 2.2306 |
| Navajo | 3 | B | PC | ESP-HS | Y | 2.7359 |
| Jack Watson | 4 | B | PC | ESP-CS |  | 2.9333 |
| Brayton Point | 1 | B | PC | ESP-CS |  | 3.2000 |
| Bay Front Plant | 5 | B | CYCLONE | MECH |  | 3.5792 |
| Brayton Point | 3 | B | PC | ESP-CS |  | 3.6979 |
| Cliffside | 1 | B | PC | ESP-HS |  | 4.3223 |
| Wabash River Generating Station | 1 + 1A | B | COAL GAS | NONE |  | 5.3343 |
| Polk Power | 1 | B | COAL GAS | NONE |  | 5.4713 |
| Gaston | 1 | B | PC | ESP-HS |  | 6.0738 |
| Port Washington | 4 | B | PC | ESP-CS |  | 6.6916 |
| Dunkirk | 2 | B | PC | ESP-HS |  | 6.8030 |
| Bruce Mansfield | 1 | B | PC | PARTSCRUB |  | 7.0985 |
| Gibson Generating Station (1099) | 3 | B | PC | ESP-CS |  | 9.7452 |
| Gibson Generating Station (0300) | 3 | B | PC | ESP-CS |  | 29.0614 |
| R.M. Heskett Station | B2 | L | FBC | ESP-CS |  | 3.9768 |
| Antelope Valley Station | B1 | L | PC | BAGHOUSE |  | 4.0042 |
| Leland Olds Station | 2 | L | CYCLONE | ESP-CS |  | 4.0233 |
| Stanton Station | 10 | L | PC | BAGHOUSE |  | 6.2517 |
| Stanton Station | 1 | L | PC | ESP-CS |  | 6.9024 |
| Coyote | 1 | L | CYCLONE | BAGHOUSE |  | 7.9523 |
| Lewis & Clark | B1 | L | PC | PARTSCRUB |  | 10.8315 |
| TNP-One | U2 | L | FBC | BAGHOUSE |  | 10.8596 |
| Limestone | LIM1 | L | PC | ESP-CS | Y | 13.6612 |
| Monticello | 3 | L | PC | ESP-CS | Y | 18.3232 |
| Big Brown | 1 | L | PC | ESP-CS/BAGHOUSE |  | 30.0889 |
| Monticello | 1 | L | PC | ESP-CS/BAGHOUSE |  | 55.8686 |
| AES Hawaii, Inc. | A | SB | FBC | BAGHOUSE |  | 0.4606 |
| Clay Boswell | 2 | SB | PC | BAGHOUSE |  | 0.6633 |
| Craig | C3 | SB | PC | BAGHOUSE |  | 0.7248 |
| Cholla | 3 | SB | PC | ESP-HS |  | 1.2066 |
| Craig | C1 | SB | PC | ESP-HS | Y | 1.4456 |
| Meramec | 4 | SB/B | PC | ESP-CS |  | 1.7255 |
| Nelson Dewey | 1 | SB/PET | CYCLONE | ESP-HS |  | 2.1349 |
| Coronado | U1B | SB | PC | ESP-HS | Y | 2.4468 |
| Comanche | 2 | SB | PC | BAGHOUSE |  | 2.5931 |
| Laramie River Station | 1 | SB | PC | ESP-CS | Y | 3.0184 |
| Cholla | 2 | SB | PC | MECH/PARTSCRUB | Y | 3.1864 |
| Laramie River Station | 3 | SB | PC | ESP-CS |  | 3.3411 |
| St. Clair Power Plant | 4 | SB/B | PC | ESP-CS |  | 3.9076 |
| Clay Boswell | 3 | SB | PC | PARTSCRUB | Y | 4.0454 |
| San Juan | 2 | SB | PC | ESP-HS | Y | 4.2854 |
| Clay Boswell | 4 | SB | PC | PARTSCRUB | Y | 4.4550 |
| Jim Bridger | BW 74 | SB | PC | ESP-CS | Y | 4.7040 |
| Presque Isle | 9 | SB | PC | ESP-HS |  | 5.0738 |
| Lawrence | 4 | SB | PC | PARTSCRUB | Y | 5.1181 |
| La Cygne | 1 | SB | CYCLONE | PARTSCRUB | Y | 5.5140 |
| Colstrip | 3 | SB | PC | PARTSCRUB | Y | 5.7264 |
| Montrose | 1 | SB | PC | ESP-CS |  | 5.8573 |
| Clifty Creek | 6 | SB/B | PC | ESP-HS |  | 6.8745 |
| Newton | 2 | SB | PC | ESP-CS |  | 6.9877 |
| Wyodak | BW 91 | SB | PC | ESP-CS |  | 7.0701 |
| Sherburne County Generating Plant | #3 | SB | PC | BAGHOUSE |  | 7.5401 |
| George Neal South | 4 | SB | PC | ESP-CS |  | 7.7269 |
| Rawhide | 101 | SB | PC | BAGHOUSE |  | 7.7630 |
| Sam Seymour | 3 | SB | PC | ESP-CS | Y | 8.6353 |
| GRDA | 2 | SB/B | PC | ESP-CS |  | 8.6918 |
| Columbia | 1 | SB | PC | ESP-HS |  | 10.3097 |
| Platte | 1 | SB | PC | ESP-HS |  | 10.6121 |
| Kline Township Cogen Facility | GEN1 | WASTE B | FBC | BAGHOUSE |  | 0.0816 |
| Scrubgrass Generating Company L.P. | GEN1 | WASTE B | FBC | BAGHOUSE |  | 0.0936 |